## Slide 1
Presented by Yimei Zhu (BNL)
On behalf of the organizers
Future of Electron Scattering and Diffraction Workshop
(FESW)
Summary
BESAC Meeting
July 30, 2014

## Slide 2
Workshop overview
Key breakthrough science opportunities and challenges
Critical enablers - major instrumentation needs
- Concluding remarks
Outline
http://science.energy.gov/bes/news-and-resources/reports/

## Slide 3
The goal:
To identify the opportunities in electron scattering and diffraction that address BES Grand Challenges.
The key question:
What are the scientific frontiers requiring advances in electron scattering and diffraction to address new science in chemistry, materials, physics & biology?
Future of Electron Scattering and Diffraction Workshop
Feb 25-26, 2014, Rockville, MD USA
Attendees:
- about 60 invited world-leading experts
in experiment, theory, instrumentation development
- representatives from NSRCs and BES managers

## Slide 4
Yimei Zhu
(BNL)
Haimei Zheng
(LBNL)
Ernie Hall
(GE)
Susanne Stemmer (UCSB)
Four organizers for four topical sessions
Ultrafast
science
Sample environment
Advances in imaging
Measuring
functionality
FESW coordinator: George N. Maracas (DOE-BES)

## Slide 5
Revolutionary Advances in
Electron Scattering, Diffraction, Imaging and Spectroscopy
Overarching Theme
What new science could be enabled by advances in electron scattering and diffraction?
Implementation
How can these advances be achieved in the next generations of instrumentation?
Focus Areas
Energy Resolution
Sample Environment Capability
How can the optimum synergies be found to produce revolutionary breakthroughs?
Spatial Resolution
New Science in
Chemistry, Materials Science, Physics, Biology
Temporal
Resolution
Ultra-Fast, Ultra-Small, Sample Environment, Measuring Functionality
Workshop Scope

## Slide 6
- The BES sponsored TEAM project has advanced imaging to 0.5Å spatial resolution
- For the future, the scientific case for improving resolution alone is not compelling
- There is a strong scientific motivation for achieving molecular/atomic resolution measurements of functionality at short time scales and in real environments to address BES Grand Challenges
A historical perspective
0
.
0
0
0
1
0
.
0
0
1
0
.
0
1
0
.
1
1
TEAM
Electron microscope
Light microscope
Aberration corrected electron microscope
Resolution (nm)
0.1
1
10
100
1000
Ross
Amiei
Abbe
Ruska
LBL ARM
Marton
1800 1840 1880 1920 1960 2000 2040
Year

## Slide 7
A
B
D
Enablers
[1, 2, 3]
Enablers
[2, 3]
Enablers
[2]
Enablers
[1, 2, 3]
C
Four science areas and three instrument enablers were identified where electron probes can have major impacts on Grand Challenges
Science Areas
[1] Multidimensional atomic resolution microscope
[2] Ultrafast electron diffraction and microscopy instrument
[3] ‘Lab-in-gap’ dynamic microscope
Instrument Enablers

## Slide 8: A. Multidimensional* Visualization of Real Materials
- Electronic and Atomic Structure:
imaging defects, dopants, impurities, vacancies in 3D
- Collective / Correlative Phenomena & Materials:
imaging atomic structure with spin, charge, and
electronic state under external stimuli
- Energy Transport at Nanoscale:
mapping phonon density of states, scattering process and correlating to atomic structure
- Mesoscale Materials and Phenomena:
imaging formation of mesoscale structures
μs – fs temporal resolution
imaging grains in a Au nanoparticle in 3D (see report)
protein tomography
*Muiltidimensional - three-dimensional atomic scale tomography and spectroscopy of atomic and electronic structures over real/momentum/energy space
Zhang, Ren, PLoS ONE,
7 30249 (2012)

## Slide 9
Example: engineer phonon scattering at nanoscale to minimize heat transport
A. Multidimensional Visualization of Real Materials
Challenge: thermoelectric energy harvesting – design materials with low phononic heat transport and high electronic conductivity (optimize ZT)
Present: phonon imaging and transport measurements at nanoscale are not practical
Siemens, et al Nat. Mat. (2009)
Nat. Nanotech. 8, 471–473 (2013)
2.5
2.0
1.5
1.0
0.5
0.0
ZT max
1940
1950
1960
1970
1980
1990
2000
2010
evolution of ZTmax over time
–importance of the ‘nanoscale’
Future:
ultrafast electrons (sub-ps) can image nanoscale phonon scattering dynamics and heat propagation
high-energy resolution (sub-10meV) enables imaging phonon density of states at nanoscale

## Slide 10
B. Atomic Scale Molecular Processes
Proton
transfer
Challenge: understand & ultimately control the selectivity and efficiency of photon energy conversion
Proton transfer coordinate
Conical
intersection
Potential energy
Example: excited state charge transfer is an important photostabilizer - which path does the molecule take in the photoexcited state?
Paterson et al., J. Phys. Chem. A 109, 7527 (2005)
Present: x-rays have low sensitivity to nuclei (Thomson scattering ~1/mass2) not feasible for revealing proton transfer
Future: fs electron diffraction can measure in real time the full molecular structure with sub-0.1Å and 10 fs resolution while the molecule relaxes

## Slide 11
Future:
- use tailored intense electric field pulses & tunable multicycle optical excitation to control superconductivity, metalicity, multiferroicity (iii) ….
- use ultrafast electron probes to disentangle locally competing order parameters
10 nm
Challenge: disentangle and control competing lattice, charge, spin, orbital order
Present:
- equilibrium phase separation as seen by nanoprobes (i).
- light-induced superconductivity seen by spatially averaging fs x-rays & THz probes (ii).
(i) superconducting gap (STM)
(ii) Light-induced superconductivity
(iii) THz pulse coupling of multiferroicity
C. Photonic Control of Emergence in Quantum Materials
For figure details see report

## Slide 12: D. Evolving Interfaces, Nucleation, and Mass Transport
(A) Catalytic Au particles on CeO2 under CO/air (see report).
(B) Pt-Fe particles growth in liquid solution (see report).
2nm
Atomic imaging and spectroscopy in vacuum,
Lopez-Bezanilla et al , J. Chem. Phys. Lett. 5, 1711 (2014).
Challenge: imaging interface dynamics, mass transport and nucleation events at molecular and atomic level in-situ and in-operando.
Present: atomic-resolution imaging and spectroscopy measurement only in vacuum and in steady state.
Future: molecular/atomic level imaging and spectroscopy in liquid, gas, during electrochemical deposition, in oxidation and corrosion in-situ and in-operando.

## Slide 13
[1] Multidimensional atomic resolution microscope
Enablers – Major New Instrumentation Needs
[3] ‘Lab-in-gap’ dynamic microscope
[2] Ultrafast electron diffraction and microscopy instrument

## Slide 14
[1] Multidimensional Atomic Resolution Electron Microscope
Accessing structural info over real/momentum/energy space @ low-temperatures
  - imaging dopants, interstitials, light elements
  - visualizing localized phonon modes and motion of charged particles/vacancies
  - correlating lattice, spin, orbital, and charge
  - accessing emergent electronic phases and radiation-sensitive materials
Uniquely suited to answer fundamental questions in condensed matter physics that require understanding of physical and electronic structure at the atomic scale.

## Slide 15
Present
spatial resolution: 0.5Å @ 300K
transmittance: 10meV @ 10mrad
stage drift rate: 15Å/min
Future
spatial resolution: <1.0Å @ 5K
transmittance: 5meV @ 20mrad
stage drift rate: 1.5Å/min
high-speed, radiation resistant, energy-resolving active pixel detector: DQE 0.7
stable cryogenic capabilities (stage stability 0.1Å)
1 meV phonon resolution spectroscopy
1eV resolution x-ray detector solid angle 4sr
Key developments required
10x improvement in gun brightness, beam energy and energy spread
DQE: Differential Quantum Efficiency
Technical challenge: developing revolutionary detectors and attaining system stability for atomic resolution at 5K
[1] Multidimensional Atomic Resolution Electron Microscope

## Slide 16
[2] Ultrafast Electron Diffraction and Microscopy Instrument
Complementary to XFEL, taking advantage of strong interaction of electrons with matter, enabling the understanding of dynamics of chemical reactions, mesoscopic systems and the photonic control of emergence in quantum materials
Imaging and controlling materials processes in real-time and real-space
  visualizing energy / mass transport over various length- and time-scales
  determining molecular pathways for photon energy conversion
  creating transient / emergent properties
  electric field control of metal-insulator transitions & multiferroic domain dynamics
  disentangling locally competing order parameters
  ps-nm imaging defect dynamics and evolution of order in non-crystalline materials

## Slide 17
Achieving a 1000 x improvement in time resolution over current microscopes
Present resolution
Diffraction: 100m probe, 300fs (stroboscopic /single shot, 105 e-)
Imaging: 5nm, 15ns (single shot, 107 e-)
Future resolution
Diffraction: 10μm probe, 10fs (stroboscopic), 100fs (single shot, 105 e-)
Imaging: 1nm, 10ps (single shot, 107 e-)
pump technology
including THz pulses
high brightness electron source
multipole lenses
novel detector
Key developments required
Technical challenge: getting sufficient electrons in the beam for single shot imaging in the presence of space charge
[2] Ultrafast Electron Diffraction and Microscopy Instrument

## Slide 18
Enabling quantitative measurements of materials structure, composition, and bonding evolution in working environment
Allows multi-modal (e.g., optical, thermal, mechanical, electrical, and electrochemical) probing of materials’ functionality in situ and in operando.
[3] ‘Lab-In-Gap’ Dynamic Microscope
  liquids, gases and plasmas; super-atmospheric pressure; biasing, cooling, heating stages; closed liquid/gas flow cells
  in-situ and in-operando experimentation of materials under real operating conditions at molecular and atomic resolution
  dynamic process and time resolved observations

## Slide 19
Molecular reactions
Graphene
encapsulant
ETEM & gas cell
Gas mixing reactions
Flow channel
Imaging biological materials
Mechanics in extreme environment
Light interaction
SiNx
liquid cell
Electric
biasing
upper pole piece
lower pole piece
electron beam
laser
Present resolution
5 mm gap @ 0.5 Å (TEAM)
gas @ 1 Torr: 1 Å − 1.4 Å, liquid drop: 2 Å
time resolution: 2.5 ms (TEAM)
Future resolution
10 mm gap @ 1 Å
gas @ 1 Torr: 1 Å, liquid: 1 Å
time resolution: 10 ns (pump/probe)
differentially pumped, corrected for spherical / chromatic aberrations
Key developments required
synergistic development of optics, source, sample environment, and detectors
Technical challenge: attaining molecular/atomic resolution in working environment
[3] ‘Lab-In-Gap’ Dynamic Microscope

## Slide 20
“To realize the proposed instruments in a timely fashion, BES should aggressively support research and development of complementary and enabling instruments, including
Advanced electron source, new detectors, optics, tunable pumps, stages
The proposed instruments would have transformative impact on physics, chemistry, materials science, engineering and technology, and other fields.”
FESW Concluding Remarks
BES is uniquely positioned to lead this effort and, with national lab resources, to provide technology breakthroughs in key development areas
Estimated development time for implementation
Near term (3 years): Ultrafast electron diffraction and microscopy instrument
Mid term (3-5 years): ‘Lab-in-gap’ dynamic microscope
Long term (5-10 years): Multidimensional atomic resolution electron microscope

## Slide 21
Thank you !
Acknowledgement
E. Hall, S. Stemmer, H. Zheng (FESW co-organizers)
G. Maracas, J. B. Murphy (DOE/BES)
X. Wang, H. Durr, M. Guehr (SLAC)
D. Muller (Cornell)
E. Stach (BNL)
J. Spence (ASU)
And all the other workshop participants