## Slide 1: BESAC Briefing on the Basic Research Needs for Environmental Management Workshop July 8–11, 2015
Sue Clark, PNNL and Washington State University
Michelle Buchanan, ORNL
Bill Wilmarth, SRNL
Andy Schwartz, DOE-BES
February 11, 2016
Advanced Scientific Computing Research (ASCR)
Biological and Environmental Research (BER)
Basic Energy Sciences (BES)

## Slide 2: Outline
Workshop Motivation
  EM Mission and Challenges
  SEAB Task Force Recommendations
Workshop Charge, Leadership, Structure
Workshop Report
  Grand Challenges
  Priority Research Directions

## Slide 3: Addressing the Nuclear Weapons Legacy
    Since 1989, EM has completed its cleanup mission at 91 of the 107 major nuclear weapons and nuclear research sites.
Historical Cleanup Sites
HI
PR
EM Historical Cleanup Sites
Remaining Cleanup Sites

## Slide 4: Significant Cleanup Challenges Remain
Safely storing highly radioactive liquid waste in over 220 underground tanks
Dispositioning radioactive, chemically hazardous waste
Remediating 93 square miles of contaminated groundwater
Maintaining a stable and skilled workforce
Retrieving over 90 million gallons of liquid radioactive waste
  Decommissioning facilities and structures

## Slide 6: EM Accomplishment and Challenge
Cost in Billion US Dollars
Fiscal Years
Profile of Historical EM Annual Costs
Average Annual Budget = $6B
Cost in Billion US Dollars
Fiscal Years
Cost Estimate Profile of EM’s Remaining Mission (2016 To 2065)
$6B Historical Budget Level
Current Lifecycle Baseline
To-Go Estimate
  $235 billion
  2065 completion
$28 billion gap
Past Investment
$152 billion spent
Completed cleanup at 91 of 107 major sites

## Slide 7: An Example: The Chemistry of High Level Radioactive Waste is Counterintuitive
High level radioactive waste characteristics are often not acceptable for pumping materials from tanks, causing significant operational risks
Slurry yield stress often does not scale with colloidal size distributions
Sonication of waste slurries can sometimes make colloids larger
Dilution of waste slurries can sometimes cause precipitation
Finely divided materials are often more refractory than larger crystalline solids
Group 5 REDOX Sludge
7

## Slide 8: SEAB Task Force Report on Technology Development for Environmental Management (Dec. 2014)
Task Force’s primary recommendations:
  Incremental technology development (EM)
  High-impact technology development (EM)
  EM university program (EM)
  Fundamental Research Program (SC)
Fundamental Research program should:
  Develop new knowledge and capabilities that bear on the EM challenges
  Be managed by the Office of Science in close coordination with EM
  Have a budget of ~$25M/year
  Commence with a workshop involving all potential participants to develop a strategic research plan to inform requests for proposals

## Slide 9
Workshop Chair: Sue Clark (PNNL/WSU)
Associate Chairs: Michelle Buchanan (ORNL)
Bill Wilmarth (SRNL)
Basic Research Needs for Environmental Management Workshop
Co-sponsored by ASCR, BER, BES; July 8–11, 2015
CHARGE: To conduct a thorough assessment of the scientific issues associated with the environmental management stewardship responsibility of DOE, and to identify scientific challenges, fundamental research opportunities, and priority research directions in the following areas:
  Waste stream characterization, transformation, and separations
  Waste form
  Contaminant fate and transport in geological environments
Plenary Session Speakers:
  Pat Dehmer, DOE-SC
  Monica Regalbuto, DOE-EM
  Richard Meserve, Covington & Burling LLP
  Andrew Felmy, PNNL
  Bill Weber, UTK
  Carl Steefel, LBNL
Breakout Sessions and Chairs:
Waste Stream Characterization, Transformation, and Separations: Jen Braley (CSM), Mark Antonio (ANL)
Waste Form: Jerry Frankel (OSU), Jim Marra (SRNL)
Contaminant Fate and Transport in Geological Environments: David Cole (OSU), Susan Hubbard (LBNL)
Crosscutting Research: Aurora Clark (WSU) & Todd Allen (INL)
Factual Document:
“Assessment of Technologies for the DOE EM Mission”
Pre-Workshop Webinars:
EM Overview: June 25, 2015
SC Overview: June 30, 2015
SC Technical Lead: Andy Schwartz (BES)

## Slide 10: Grand Challenge 1: Interrogation of inaccessible environments over extremes of time and space
Current efforts are stymied by limited ability to safely and confidently assess existing containment structures, waste forms, and environmental contamination
Innovations to enable assessment of the inaccessible:
  Combine advances in imaging capabilities, remote and in-situ sensing, and data analytics, to characterize extreme environments
  Support decision making processes by understanding and controlling composition, structure, reactivity, and transport, from fractions of a second to millennia, from atoms to kilometers
Data Analytics
Field Scale Remote Sensing
Interrogation of HL Waste Tanks

## Slide 11: Grand Challenge 2: Understanding and exploiting interfacial phenomena in extreme environments
Unprecedented extremes in complexity, harshness, space, and time impede progress toward radioactive waste processing, disposal, and environmental remediation
Elucidate how interfacial phenomena in highly heterogeneous environments dictate system properties and functionality
  Will enable improved engineering of processing strategies, waste form designs, and subsurface containment and cleanup
Understand interfacial phenomena in extreme environments
  Will lead to new separations methods, new materials for waste forms, and new control of subsurface contamination
Radionuclide Partitioning at Solid:Liquid Interfaces

## Slide 12: Why Now?
Over the past decade, incredible strides have been made in nanoscale materials science, computing, imaging, biogeochemical system science, and analytics, creating opportunities to:
  Pursue complexity and heterogeneity
  Span unprecedented scales of time and space
  Access and assess the inaccessible
The time is ripe to apply these advances to radiation environments and radioactive materials
Light sources, computational tools, and other state-of-the-art facilities are available to enable research success

## Slide 13: Priority Research Directions
Elucidating and exploiting complex speciation and reactivity far from equilibrium
Understanding and controlling chemical and physical processes at interfaces
Harnessing physical and chemical processes to revolutionize separations
Mechanisms of materials degradation in harsh environments
Mastering hierarchical structures to tailor waste forms
Predictive understanding of subsurface system behavior and response to perturbations
Transformative Research Capabilities

## Slide 14: Elucidating and exploiting complex speciation and reactivity far from equilibrium
Research Needs
Technology Impact
Persistent Transients
Scientific Challenges
Identifying and controlling chemical reactivity and reaction networks for complex systems in extreme environments
Understanding radiolysis and radiation effects to predict unique species in radioactive waste systems
Prediction and control of speciation in radioactive waste streams, waste forms, and subsurface environments
Transforming radioactive waste processing schemes
New approaches for characterization of inaccessible environments
Mastering complex chemistry far from equilibrium
Understanding and exploiting chemical reactivity under extreme conditions
Expanding our knowledge on the coupling of radiation and chemical effects in matter

## Slide 15: Understanding and controlling chemical and physical processes at interfaces
Research Needs
Technology Impact
Organization at Solid:Liquid Interface
Scientific Challenges
15
Predicting and exploiting chemical and physical structure at interfaces
Behavior of water in confined environments at interfaces
Particle-particle interactions in concentrated electrolytes and other extreme conditions
Ability to process radioactive waste streams that have consistencies of gels and pastes
Predict changes in waste streams that can lead to agglomeration and precipitation
Improved models to anticipate performance of waste treatment schemes and subsurface remediation approaches
Identifying the chemical and physical processes at interfaces under extreme conditions
Understanding solvent behavior in constrained environments
Linking interfacial reactivity with macroscopic properties

## Slide 16: Harnessing physical and chemical processes to revolutionize separations
Research Needs
Technology Impact
Templating Structures with Anions
Scientific Challenges
16
Isolating risk-driving radionuclides from bulk waste stream components to minimize radioactive waste volumes
Driving selectivity by exploiting coordination chemistry, matrix interactions, and radiolysis
Avoiding or exploiting self-assembly and third phase formation
New classes of molecules and molecular architectures for highly efficient separations
Atom efficient separations that are highly selective under extreme conditions
New separations media that are resilient to extreme conditions
Understanding mechanisms that drive separations at solid:liquid and liquid:liquid interfaces
Design and synthesis of molecular architectures with tailored properties
New approaches for separations based on physical and chemical properties

## Slide 17: Mechanisms of materials degradation in harsh environments
Research Needs
Technology Impacts
Dynamic Imaging of Glass Corrosion
Scientific Challenges
17
Materials performance under extreme conditions of concentrated electrolytes, high alkalinity, and ionizing radiation
Identifying mechanisms of materials degradation in extreme environments
Anticipate materials degradation and failure over extremely long time periods
Develop revolutionary new corrosion resistant materials with design lifetimes of millennia
Enable direct disposal of DOE-owned spent nuclear fuel and lifetime extensions of existing nuclear reactors
Understanding the coupling of radiation and electrochemical processes in complex systems
Identifying mechanisms of materials degradation in harsh environments
Determining molecular level corrosion mechanisms in constricted volumes

## Slide 18: Mastering hierarchical structures to tailor waste forms
Research Needs
Technology Impacts
Molecular Design for Waste Forms
Scientific Challenges
18
Radioactive waste forms must retain waste constituents for millennia
They are enormously complex chemical systems that evolve with time
Hierarchical structures can be designed for long-term performance.
Revolutionary new materials tailored for radioactive waste disposal
New pathways for design and discovery of material architectures with desired behaviors
Predictive models for waste form performance over extended time domains
Design of new material architectures with desired behaviors
Linking molecular level phenomena to macroscale behavior over eons
Extending atomistic, thermomechanical, and structural modeling to predict physicochemical properties

## Slide 19: Predictive understanding of subsurface system behavior and response to perturbations
Research Needs
Linking system behavior to appropriate scale
Technology Impacts
Scientific Challenges
19
Understanding subsurface spatial properties over a continuum of scales
Anticipating the impact of perturbations over a continuum of temporal scales
Impact of strong chemical gradients and microenvironments on contaminant behavior
Improved design of remediation systems for long-term performance
Anticipate transient and/or emergent behaviors in the subsurface environment
New multi-scale, process-rich models for reactive transport in the subsurface
Quantifying time scales of transient events in the subsurface environment
Elucidating process interactions within hierarchical connected pore structures
Computational methods for adaptive, cross-scale models in time and space

## Slide 20: Transformative Research Capabilities
Research Needs
Scientific Challenges
20
Multi-dimensional characterization of extreme, dynamic, and inaccessible environments
Integrated simulation and data-enabled discovery
High sensitivity, high fidelity ex-situ characterization
Information rich in-situ and remote characterization
Data enabled discovery
Advanced simulation and modeling with predictive capabilities
Porosity Evolution and Contaminant Release
Technology Impacts
Progress towards prediction for highly complex systems
Incredible new characterization approaches that provide insights via remote, ex-situ, and/or in-situ measurements
Greater confidence in prediction over extremes in space and time

## Slide 21: BRN Agenda
Initial Report Writing: 4:00pm, Friday – Noon, Saturday

## Slide 22: Workshop Participants
Panel 1 – Waste Stream
Jenifer Braley, CSM (co-chair)
Mark Antonio, ANL (co-chair)
Sam Bryan, PNNL
Rebecca Chamberlain, LANL
Ken Czerwinski, TerraPower/UNLV
Lætitia Delmau, ORNL
David Dixon, University of Alabama
Ross Ellis, ANL
Andrew Felmy, PNNL/WSU
Nathaniel Fisch, PPPL/Princeton
Amy Hixon, Notre Dame
Gregg Lumetta, PNNL
Luther McDonald, Utah
Thom Orlando, GA Tech
Alena Paulenova, Oregon State U
Reid Peterson, PNNL
Brian Powell, Clemson
Ralf Sudowe, UNLV
Justin Walensky, Missouri
Panel 2 – Waste Form
Gerald Frankel, Ohio State (co-chair)
Jim Marra, SRNL (co-chair)
Theodore Besmann, South Carolina
Brady Hanson, PNNL
Carol Jantzen, SRNL
Meimei Li, ANL
Elizabeth Opila, Univ. of Virginia
Ivar Reimanis, CSM
Ian Robertson, Wisconsin
Kurt Sickafus, U. Tennessee
Bob Sindelar, SRNL
Narasi Sridhar, FNACE
Blas Uberuaga, LANL
John Vienna, PNNL
Bill Weber, U. Tennessee/ORNL
Panel 3 – Contaminant Fate and Transport
David Cole, OSU (co-chair)
Susan Hubbard, LBNL (co-chair)
John Bargar, SLAC
Ian Bourg, Princeton
Miles Denham, SRNL
Young-Shin Jun, Wash. U, St. Louis
Annie Kersting, LLNL
Kate Maher, Stanford
David Moulton, LANL
Fred Phillips, New Mexico Tech
Eric Roden, Wisconsin
Kevin Rosso, PNNL
Tim Scheibe, PNNL
Lee Slater, Rutgers
Carl Steefel , LBNL
Dave Wesolowski, ORNL
Ken Williams, LBNL
Kelly Wrighton, Ohio State
John Zachara, PNNL
Panel 4 - Crosscutting
Aurora Clark, WSU (co-chair)
Todd Allen, INL (co-chair)
Bill Casey, UC Davis
Lynne Ecker, BNL
Michael Demkowicz, MIT
Tom Doe, Golder Associates
Maik Lang, U. Tennessee
David Shuh, LBNL